## Slide 1: Digital Transformation of SATCOM Networks
Juan Deaton

## Slide 2: Hello!
Juan Deaton, Ph.D.
  jdeaton@envistacom.com
Bio:
    Dr. Juan Deaton is currently a research scientist at Envistacom, where he is using his 20 years of telecom experience and research to build virtualized transport satellite systems. In his previous employment with Comtech EF Data, he was engaged in variety of different types of research like anti-jam waveforms, satellite channel models, and developing LDPC codes for Versa FEC 2. Before working at Comtech EF Data, he worked for the Idaho National Lab, where he researched spectrum optimization, spectrum modeling, and emergency communications. Before the INL, Juan worked for Motorola’s CDMA network division, where he was the recipient of the 2005 CDMA quality award for developing hands-on training for CDMA cellular equipment deployments. His patented and published work includes spectrum sharing in cellular networks, wireless airborne emergency communications, and mobile advertising. His M.S. and Ph.D. degrees were earned from Virginia Tech and BSEE from the University of Idaho.

## Slide 3: Introduction
Purpose
  The purpose of this brief is to explain the digital transformation of SATCOM.
Outline
  Introduction
  Digitization of SATCOM Networks
  Virtualization of SATCOM Networks
  Use Cases

## Slide 4
“It is not the strongest of the species that survives, nor the most intelligent that survives. It is the one that is most adaptable to change.”
Charles Darwin
Introductions

## Slide 5: Motivation
Rapidly Changing Space Layer
  New LEO, MEO, and GEOs
Demand for SATCOM
  21% CAGR
Stove-Piped, Isolated Systems
  Independently non-interoperable systems

## Slide 6: DoD SATCOM Complexity and Variegation
50,000 Active Satellites in the Next 10 Years
17,000 DoD Terminals
135 Different Types

## Slide 7: Key Demands for SATCOM Networks
Key Demand-1
Freedom From Vendor Lock-in
Proprietary-based modems complicate networks, logistics, migration, increase costs, and contribute to stove-piped systems. Vendor lock-in business models are an antiquated way of doing business that form rigid oligopolies that limit innovation and technology progression.
Key Demand-2
Reduction in Total Cost of Ownership (TCO)
Operating and capital expenses are key drivers in network sustainability. In commercial networks, managing SATCOM networks’ costs is important in maintaining profitability. In DoD networks, managing SATCOM networks’ costs is important in maintaining network longevity.
Key Demand-3
Ground Segment Sustainability
Operational complexity adds cost and increases logistical footprint, which creates upgrade stagnation. Migration paths to new technology should have minimal network impacts.
Key Demand-4
Terminal/Modem Agility
Terminal segments, along with their antennas, need to operate on multiple waveforms, bands, and orbits. Modems should also operate on a variety of waveforms.
Key Demand-5
System Agility/Resiliency
SATCOM ground and terminal segments should deploy automated configurations based on mission needs, maintained connectivity through contested environments, and changing network demand.
Key Demand-6
High Computational Density/Efficiency
The demand for reduced size, weight, and power (SWaP) is ever present. Rack space in many networks is reaching capacity, creating additional operational costs to meet the increasing demand for throughput.
Notes: Idirect – I support depends on how much hubs yo uhave 1.4/ 1.6 M a yuear to support network
Current card swill last 2/3 revs before needing to buy new hardware, 3-5 all hardware needs to be replace and rigged game. Apple iPhone battery analogy
More bandwidth with smaller about of footprint with same amount of capability.
Had held modem that fits in your hand that fits in your hand. You can fit a lot of those in hand and fit a lot in rack and another works in case.
USB philosophy, Hub will be able to redirect onto a new transponder, without manual intervention.
Idirect has a key feature that has good global management that does the worldwide network to move from transponder to transponder, terminals that can move locations and change to new birds.
Global management of all terminals in the network everything that comes up in the network. STS Codemettle has some growth, all have issues . Real estate and power are the most expensive things STT we don’t want to pay for an ACU. RHN we need to use a different antennas.

## Slide 8: Components of the Digital Transformation
Digital Transformation
Virtualization
Hybrid
Cloud
Advanced
Antennas
Common Hardware Platforms
Digitization
Digital IF Modem
Edge Device
Digital IF Protocol
NFV
OSS/BSS
MANO

## Slide 9: Traditional vs. Digitized
Baseband Modem
RF Front End
10101011
TX
RX
L-band IF
RF
Modem
RF Transmission
10101011
Digital IF Modem
TX
RX
Edge Device
L-band IF

RF
Digital IF
IP Data
IP Data

## Slide 10: Virtualization Overview
Virtualized Infrastructure
Virtualized Environment
MEM
RAM
CPU
NIC
Waveform
VNF-1
WAN Accel
VNF-2
QoS
VNF-3
10101011
Digital IF Modem
Notes: Different to moving to PC for what OS you want to load on it. Apps like a iPhone. Multiple vendors will join in and everything will get cheaper and become commondity products.

## Slide 11
“The first step to this dynamic ground architecture is replacing existing analog Intermediate Frequency (IF) interfaces with an open, interoperable digital standard ...”
Maj. Gen. Lawrence A. Stutzriem, USAF (Ret.)
Digitization of SATCOM Networks

## Slide 12: Digitization of SATCOM Networks
Digital Transformation
Virtualization
Hybrid
Cloud
Advanced
Antennas
Common Hardware Platforms
Digitization
Digital IF Modem
Edge Device
Digital IF Protocol
NFV
OSS/BSS
MANO

## Slide 13: Digitized Architecture
10101011
Digital IF Modem
TX
RX
Edge Device
L-band IF
Digital IF
IP Data

## Slide 14: Ground Segment Gateway
L-band IF
L-Band
Switching System

RF
Proprietary Modem Bank


IFL
~1000 ft
IFL
~100 ft
Electronics Equipment Building
Shelter
RF Transmission
Switch Matrix
Combiner/Splitter
External Data
Networks
Notes: TT&C another gateway for doing TT&C and separate. Controls uses the internet databased to update ephemeris. Move to LEO they will need to get a Ephemeris. ACU can’t touch the antenna. There need for an data base. ACU Leo, John Lane was out there to figure out how the ephemeris gets entered in. Ground segment is separate from TT&C networks.

## Slide 15: Digitized Ground Segment
Remote Site
Digital IF
WAN

DIFL
Unlimited
Edge Devices
DIFL
2-40 km
Local Teleport EEB


External Data
Networks
Digital IF
Modem Bank
Digital IF
LAN
100/400 GbE
Local Sites


## Slide 16: Ground Station as a Service (GSaaS)
VITA 49.2
Proprietary
Digital IF
Data Products
Edge
Device
Waveform
Processing
Storage
10G
<100 MHz
Digital IF
Stack
802.3
UDP/IP
RTP
VITA 49.2

## Slide 17: Enterprise Digital IF Multi-Carrier Modem (EDIM)
Digital IF
DMB
L-band
Edge Device

RF


L-band IF
DAD
External Data
Networks
Digital IF
Remote Site
Digital IF
WAN


## Slide 18: DIFI Protocol Stack
Transport
Physical
Data Link
802.3
UDP/IP
OSI
Stack
v1.0
Session
TBD
Flow Control: Reliable, low latency
Packet Loss Recovery: Retransmissions, forward erasure correction
Security: Authentication, encryption
Standard IP-Based Protocols
Data
VITA 49.2
Data representation of digital samples, context, timing, and control.

## Slide 19: Key Challenges With Digital IF Transport
Flow Control
  Definition:
    The ability to deliver digital sample packets at a rate match to the sample rate of the consumer
  Buffer-flow problem:
    Packets are received too fast or slow such that the digital sample consumer receives gaps in transmission
  Techniques:
    Backpressure in L2 switched networks using 802.3 priority pause frames
    Timestamping and clock synchronization between transmitter and receiver for L3 routed networks
Packet Loss Recovery
  Definition:
    The ability to recover lost packets in the network in time to guarantee reliable delivery with minimal latency
  Techniques:
    Retransmissions of lost packets is used by TCP to guarantee reliable transport
    Packet FEC minimizes the need for retransmissions by sending extra packets for data reconstruction
Security
  Definition:
    The protection from interception or redirection of digital streams data
  Techniques:
    AES and authentication

## Slide 20
“...the [SATCOM] enterprise needs to improve its resiliency, robustness, flexibility, and manageability.”
William J. Liquori Jr., Major General, USAF
Virtualization of SATCOM Networks

## Slide 21: Digitization of SATCOM Networks
Digital Transformation
Virtualization
Hybrid
Cloud
Advanced
Antennas
Common Hardware Platforms
Digitization
Digital IF Modem
Edge Device
Digital IF Protocol
NFV
OSS/BSS
MANO

## Slide 22: Virtualization Overview
Common
Hardware
Operating System
Application
Common
Hardware
Hypervisor
OS
App
OS
App
OS
App
OS
App

## Slide 23: Network Function Virtualization Architecture
NFVI
VNF
OSS/BSS
CPU
CPU
Storage
CPU
CPU
Network
CPU
CPU
CPU
Network
Configuration
Portal
Billing
Accounts
Application
Portal
VNF 1
Virtual
Network
VNF 2
VNF 3
VNF
4
Hypervisor
Service
Orchestrator
VNF
Manager
Infrastructure
Manager
MANO

## Slide 24: Virtualized Ground Segment
VNF
VN
Network Management System
NFVI
Edge Devices


DMB
DIL

RF Transmission
OSS/BSS
Service
Orchestrator
VNF
Manager
Infrastructure
Manager
MANO
Network
Configuration
Portal
Billing
Accounts
Application
Portal
Virtual Network
& SATCOM
Functions
Digital IF
Transport Hosts
Hypervisor

## Slide 25: OSS/BSS
NFVI
MANO
OSS/BSS
User / Operator
VNF
Digital IF Host
SD-WAN
Virtual
Waveform
Digital IF VLAN
1. Service Order
2. Service Chain Request
4. Create and Configure
Service Chain
3. Allocate and
Configure
Resources
5. Service Confirmation
6. Monitoring and Control

## Slide 26
“User terminals will be capable of multi-band and multi-waveform operations, whenever possible, to support agile, ‘path-agnostic’ connectivity, reducing vulnerability to interference and jamming.”
William J. Liquori Jr., Major General, USAF
Use Cases

## Slide 27: Modem/Terminal Agility
SAT-1
SAT-2
NFVI
VNF
MANO
Wave-1
Wave-2
Wave-N
Monitor
AI Class
Wave-1
Monitor
Wave-2
AI Class
DMB
DIL
DTS-1
DTS-2
Gateway
NFVI
VNF
Wave-1
Monitor
Wave-2
AI Class
MANO
Wave-1
Wave-2
Wave-N
Monitor
AI Class
DM
DIL
Terminal-1
NFVI
DM
DIL
Terminal-2

## Slide 28: System Agility/Resiliency
DIFL
NFVI
Remote Gateway
NFVI
Local Gateway
SAT-1
SAT-2
SAT-3
Terminal-3
NFVI
NFVI
Terminal-1
NFVI
Terminal-2